## Slide 1: Facilitating Linux Kernel Heap Vulnerability Exploitation: an idea
韩天硕

## Slide 2: Table of Content
Overview
Example & Enlights
Related work
unsolved challenges & thingking
Possible Solution

## Slide 3: Overview
Kernel heap vulnerability form:
  double free
  use after free
  out of bound read / write
  .....

## Slide 4: Overview
Kernel heap vulnerability capability model:
  the chunk size
  readable/writable bytes within(around) the chunk

## Slide 5: Overview
General pattern to exploit a heap vul model:
  identify an useful kernel object from kernel code space
  allocate such an object to region under control
  untilizing an execution path(related to the object) to finish exploition / help with exploitation

## Slide 6: Overview
General patterns to exploit a heap vul model:
  identify an useful kernel object from kernel code space
  allocate such an object to region under control
  untilizing an execution path(related to the object) to finish exploition / help with exploitation
all are unsolved challenges

## Slide 7: Overview
I want to build a database/tool that, given a vul model, can indicate me: what can be done with such a model
more specifically:
  list candidate objects, that can fit in the evil chunk size and may be useful for exploitation
  syscall sequences to allocate such useful objects
  list the objects’ capability and syscall sequences to trigger

## Slide 8: Example1
0CTF 2021 Final - kernote

## Slide 9: Example1
0CTF 2021 Final - kernote
vulnerability model:
  chunk size: one kmalloc-32 chunk
  readable bytes: none
  writable bytes: the first 8 bytes
exploitation: ldt_struct

## Slide 10: Example1
0CTF 2021 Final - kernote

## Slide 11: Example1
0CTF 2021 Final - kernote

## Slide 12: Example1
0CTF 2021 Final - kernote
two solves during the contest, both unintended:
  @Balsn gave a 1-day exp, unrelated to the vulnerability at all
  @Organizor gave a kernel ROP solve, too delicate and complicated to reproduce
conclusion: Identifying proper structs and its useful execution path is vital for kernel heap exploitation

## Slide 13: Example1
0CTF 2021 Final - kernote
Q1: where do these structs and execution path come from?

## Slide 14: Example2
CVE-2021-26708
vulnerability model:
  chunk size: one kmalloc-64 chunk
  readable bytes: none
  writable bytes: 4 bytes at offset 40

## Slide 15: Example2
CVE-2021-26708
the pointer security is at offset 40, and it will be passed to kfree() resulting to arbitrary free, and can be transformed into UAF

## Slide 16: Example2
CVE-2021-26708
Combining with the vul other capabilities, the vulnerability pattern can be transformed:
  UAF size: one kmalloc-64 chunk
  readable bytes: none
  writable bytes: the first 40 bytes

## Slide 17: Example2
CVE-2021-26708
Conclusion: some execution path does not follow general exploitation paradigm, but may work at specific vul context
Q2: finding such execution path needs extensive expertise in kernel and intensive manual efforts. Can it be automatized?

## Slide 18: Example3
QWB2021 - notebook
vulnerability model:
  UAF size: one kmalloc-0x400 chunk
  readable bytes: the first 0x60 bytes
  writable bytes: the first 0x60 bytes

## Slide 19: Example3
QWB2021 - notebook
a fancy function, available in kernels who enable multi-cpu support:
after compilation:

## Slide 20: Example3
QWB2021 - notebook
perfect for us to execute commit_creds(prepare_kernel_cred(0))
  hijack ioctl() of a tty struct to work_for_cpu_fn()
  set tty_struct[4]=prepare_kernel_cred, tty_struct[5]=0
  invoke ioctl() and the new generated cred struct will be placed at tty_struct[6], and we can read it
  do the trick again to invoke commit_creds()

## Slide 21: Example3
QWB2021 - notebook
conclusion 1: execution path of exploit is not limited to syscall sequences, sometimes can be subtle.
conclusion 2: overread is as important as overwrite.
Q3: by taking extra dimensions of vul capability into consideration, is it possible to identify more exploit paradigm?

## Slide 22: Related Work
Wu, W., Chen, Y., Xu, J., Xing, X., Gong, X., & Zou, W. (2018). FUZE: Towards facilitating exploit generation for kernel use-after-free vulnerabilities. Proceedings of the 27th USENIX Security Symposium, 781–797.
Chen, Y., & Xing, X. (2019). Slake: Facilitating slab manipulation for exploiting vulnerabilities in the linux kernel. Proceedings of the ACM Conference on Computer and Communications Security
Chen, Y., Lin, Z., & Xing, X. (2020). A Systematic Study of Elastic Objects in Kernel Exploitation. Proceedings of the ACM Conference on Computer and Communications Security

## Slide 23: Related Work: SLAKE
SLAKE: identify kernel objects that enclose at least one function pointer, then filter out objects that may be utilized for RIP hijacking
the object can be allocated from user land
the function pointer can be called from user land

## Slide 24: Related Work: SLAKE
e.g.

## Slide 25: Related Work: SLAKE
SLAKE answered such a question: I have a heap chunk overwrite primitive and I want to do a RIP hijacking, how can I do it?
The identified useful kernel objects are stored in a database, and will be paired with vul capability model

## Slide 26: Related Work: SLAKE
SLAKE vul capability model

## Slide 27: Related Work: ELOISE
ELOISE: focuses on elastic kernel objects, identify kernel objects and execution path for kernel space memory leaking
ELOISE answerd such a question: I have a kernel heap chunk overwrite primitive and I want to do a kernel space memory leaking, how can I do it?

## Slide 28: Related Work: ELOISE
e.g.

## Slide 29: Unsolved challgenges & thinking
1. there is a great number of exploitation paradigms, besides RIP hijacking and kernel space memory leaking
reading kernel space memory to a readable region(besides transfer them directly to user space)
kernel space memory overwrite
arbitrary kfree()
leaking not by elastic objects
critical kernel data corruption
spraying data into kernel heap chunk
.....
digging the kernel according to known exploitation paradigms can be inefficient and unscaleble

## Slide 30: Unsolved challgenges & thinking
2. the vul capability model is inadequate to fully describe a vul’s capability
chunk size
writable bytes
chunk size
chunk number I can control
times I can control for the same chunk
is the chunk at same address
writable bytes
times I can write
readble bytes
times I can read
.....
stronger the vul capability indicates more possible exploitation path

## Slide 31: Unsolved challgenges & thinking
3. in many situations, I only know the vul capability at hand, I have no idea what to do next
CVE-2021-26708 vulnerability model:
  chunk size: one kmalloc-64 chunk
  readable bytes: none
  writable bytes: 4 bytes at offset 40
RIP hijacking is impossible
kernel memory leaking is unlikely to work
what I do with this primitive?
knowing what can be done with a vul primitive can greatly indicate how to perform exploit

## Slide 32: Possible Solution
loose the constraint
SLAKE and ELOISE digs the kernel strictly subject to constraints, to make sure the found objects and syscall sequences follows the desired exploitation paradigm

## Slide 33: Possible Solution
mining the kernel not according to known exploitation paradigms, but by considering value and reachability
value: heuristicly definning valuable operations
reachability: filter out operations can be triggerd by syscall sequences from user land

## Slide 34: Possible Solution
value:
definning valuable operations: memory read/write, call/jmp, critical kernel functions like kfree(), .....
mark controllable bytes as taint source / symbolic value
checking if valuable operations can be tainted / controlled by symbolic values

## Slide 35: Possible Solution
reachability:
identify all valuable operation sites in execution path related to the kernel object
fuzz syscalls, until valuable operation sites reached

## Slide 36: Possible Solution
mark all fields in this struct as taint source
fuzz the kernel until found kfree() is tainted by security
e.g. find the arbitrary free() primitive in CVE-2021-26708

## Slide 37: Possible Solution
store identified kernel objects, syscalls and corresponding capability in a database, and give an algorithm that retrieve information from the database. Given a vul model such a database can:
greatly indicate exploitation path by knowing all possible operations
give indications on how to implement an eploitation path

## Slide 38
Thanks!